## Slide 1: SDN based Network Management in Emulated Environment
Submitted by: Harshal Rajan Vaze
Matriculation no.: 1269879
First examiner: Prof. Dr. Ulrich Trick
Second examiner: Prof. Dr. Armin Lehmann
External supervisor: Dr. Peter Gröschke

## Slide 2: Agenda
SDN Architecture
Different SDN Architectures
Open-source SDN Controllers
Open vSwitch
OpenFlow
Creation of Flow rules
Creations of Intents
Use-cases

## Slide 3: SDN Architecture
Application & Service Layer
Application Plane
Control Layer
Controller Plane
Infrastructure Layer
Data Plane
Network
Elements
SDN
Controller
SDN
Applications
Northbound Interface
Southbound Interface
REST API
OpenFlow, BGP, NetConf
Eastbound Interface
Westbound Interface

## Slide 4: Different SDN Architectures (1/3)
a. Physically-centralised architecture
b. Physically-distributed architecture

## Slide 5: Different SDN Architectures (2/3)
c. Physically-distributed & Logically-centralised architecture
d. Physically-distributed & Logically-distributed architecture
Act like a single controller for network

## Slide 6: Different SDN Architectures (3/3)
Root controller
e. Flat architecture
f. Hierarchical architecture

## Slide 7
Applications
North-bound (Consumer) API
Core
(Modules, Subsystems)
South-bound (Provider) API
Providers
(Link, Flow, Device, Host)
Protocols
Network Elements
ONOS Controller

## Slide 8
Applications, Orchestration
North-bound API
South-bound API
Network Elements
OpenDaylight
Platform Services
AAA
Data Exchange
Infrastructure utilities
Built-in Applications
Layer 2 Switch
Virtual Tenant Network
Network Services
LISP service
Group-based policy
Application layer traffic optimization
Platform (MD-SAL, YANG tools)
OpenDaylight Controller

## Slide 9
Applications, Operator, OpenStack cloud orchestration
North-bound API
South-bound API
Network Elements
Ryu Framework
Built-in Applications: tenant isolation, layer2 switch
Libraries: topology discovery, OpenFlow REST
OpenFlow protocols parser/ serializer
OpenFlow, OF-config
Non-OpenFlow protocols parser/ serializer
NetConf, NetFlow, VRRP
Ryu Controller

## Slide 10
Flow Tables
ovs-vswitchd
ovsdb-server
Controller
OpenFlow
Protocol
User Space
Open vSwitch
Kernel module
OVSDB Management
Protocol
OVSDB Management
Protocol
Netlink
In-Port
Out-Port
Kernel
Management

## Slide 11
Flow Table 0
Group Table
Meter Table
OpenFlow
Channel
OpenFlow
Channel
Flow Table n
Flow Table 1
Port
Port
. . .
Controller 1
Controller 2
OpenFlow
OpenFlow Switch
Pipeline
Datapath
Control Channel
OpenFlow Protocol

## Slide 12: SDN network emulators
GNS3
Mininet

## Slide 13: Flow Rules
Demo

## Slide 14
Flow
Table
0
Ingress Port
Egress Port
Flow
Table
1
Flow
Table
n
Execute Action Set
Packet
In
Packet
Out
Open vSwitch
. . .
Action Set
Action Set
Action Set
Action Set
Match Fields:
Ingress port +
Packet header +
metadata
Packet transmission through flow tables within an Open vSwitch

## Slide 15: Intent
Demo

## Slide 16
Demo
Use Case-1: Testing the ONOS Controller with Isolated Layer 2 Overlay Networks

## Slide 17
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
eth4
eth14
eth1
eth1
eth1
eth3
eth2
eth2
eth2
eth2
OVS-2
OVS-6
OVS-8
OVS-4
eth1
eth4
eth1
eth5
eth14
eth14
eth14
eth14
eth14
eth3
eth5
eth4
eth3
eth5
eth3
eth3
eth2
eth1
eth3
eth2
eth4
eth5
eth1
eth3
eth2
eth1
eth3
eth2
10.0.0.2/24
10.0.0.3/24
10.0.0.10/24
10.0.0.11/24
10.0.0.12/24
H1
H2
H3
Server1
Server2
Server3
Intent

## Slide 18
ONOS-1
ONOS-3
ONOS-2
Atomix-1
Atomix-3
Atomix-2
172.17.0.2
172.17.0.3
172.17.0.4
172.17.0.5
172.17.0.6
172.17.0.7
Raft protocol
Use Case-2: Testing the Network with Multiple ONOS Controllers
Demo
Underlying network

## Slide 19
Use Case-3: Testing the ONOS Controller with IPv6 Addressing
Demo

## Slide 20
Intent

## Slide 21
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
OVS-2
OVS-8
OVS-4
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
50.0.0.1/24
60.0.0.1/24
.2
.1
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
AS 100
AS 200
AS 300
AS 400
Border R4
Border R2
Border R3
Border R1
Internal R5
Internal R6
Controller
BGP Speaker
Use Case-4: Integrating Software-defined Network with the Legacy Networks
Demo
SDN
AS 500

## Slide 22
Single-point to single-point intents
These are uni-directional intents used to establish the BGP peering session between the external routers and the SDN BGP speakers. Each Intent connects two single attachment points in the SDN network. Each attachment point contains the following information: SDN switch DPID and switch port, and the MAC address of the attached BGP speaker/router.
Multi-point to single-point intents
These are uni-directional intents used to connect the hosts of the external networks together. Each intent is associated with an IP prefix (the IP destination), and connects the ingress attachment points of the SDN network with a single egress attachment point - the best next-hop router toward the destination IP prefix. At the ingress edge of the SDN network, an IP packet is matched on the IP destination address. The forwarding entry for the best (longest network prefix) match is selected to forward the packet toward the corresponding egress attachment point. In addition, right before the packet is forwarded, the “change destination MAC address” action is applied such that the data packet will contain the MAC address of the egress IP router toward the destination.

## Slide 25: SDN network components
Open vSwitch
OpenFlow

## Slide 26: SDN Architecture
Application Layer
Control Layer
Infrastructure Layer
Software-defined Network (centralised control)
Traditional Network (distributed control)
Embedded controlling and forwarding device
Northbound Interface
Southbound Interface

## Slide 27
Use Case-4: Integrating Software-defined Network with the Legacy Networks

## Slide 28
Use Case-2: Testing the Network with Multiple ONOS Controllers