## Slide 1: SDN based Network Management in Emulated Environment
Submitted by: Harshal Rajan Vaze
Matriculation no.: 1269879
First examiner: Prof. Dr. Ulrich Trick
Second examiner: Prof. Dr. Armin Lehmann
External supervisor: Dr. Peter Gröschke

## Slide 2: Agenda
SDN Architecture
Different SDN Architectures
Open-source SDN Controllers
Open vSwitch
OpenFlow
Creation of Flows
Creations of Intents
Use-cases

## Slide 3: SDN Architecture
Application & Service Layer
Application Plane
Control Layer
Controller Plane
Infrastructure Layer
Data Plane
Network
Elements
SDN
Controller
SDN
Applications
Northbound Interface
Southbound Interface
REST API
OpenFlow, BGP, NetConf
Eastbound Interface
Westbound Interface

## Slide 4: Different SDN Architectures (1/3)
a. Physically-centralised architecture
b. Physically-distributed architecture

## Slide 5: Different SDN Architectures (2/3)
c. Physically-distributed & Logically-centralised architecture
d. Physically-distributed & Logically-distributed architecture
Act like a single controller for network

## Slide 6: Different SDN Architectures (3/3)
Root controller
e. Flat architecture
f. Hierarchical architecture

## Slide 7
Applications
North-bound (Consumer) API
Core
(Modules, Subsystems)
South-bound (Provider) API
Providers
(Link, Flow, Device, Host)
Protocols
Network Elements
ONOS Controller

## Slide 8
Applications, Orchestration
North-bound API
South-bound API
Network Elements
OpenDaylight
Platform Services
AAA
Data Exchange
Infrastructure utilities
Built-in Applications
Layer 2 Switch
Virtual Tenant Network
Network Services
LISP service
Group-based policy
Application layer traffic optimization
Platform (MD-SAL, YANG tools)
OpenDaylight Controller

## Slide 9
Applications, Operator, OpenStack cloud orchestration
North-bound API
South-bound API
Network Elements
Ryu Framework
Built-in Applications: tenant isolation, layer2 switch
Libraries: topology discovery, OpenFlow REST
OpenFlow protocols parser/ serializer
OpenFlow, OF-config
Non-OpenFlow protocols parser/ serializer
NetConf, NetFlow, VRRP
Ryu Controller

## Slide 10
Flow Tables
ovs-vswitchd
ovsdb-server
Controller
OpenFlow
Protocol
User Space
Open vSwitch
Kernel module
OVSDB Management
Protocol
OVSDB Management
Protocol
Netlink
In-Port
Out-Port
Kernel
Management

## Slide 11
Flow Table 0
Group Table
Meter Table
OpenFlow
Channel
OpenFlow
Channel
Flow Table n
Flow Table 1
Port
Port
. . .
Controller 1
Controller 2
OpenFlow
OpenFlow Switch
Pipeline
Datapath
Control Channel
OpenFlow Protocol

## Slide 12: SDN network emulators
GNS3
Mininet

## Slide 13: Flow Rules

## Slide 14
Flow
Table
0
Ingress Port
Egress Port
Flow
Table
1
Flow
Table
n
Execute Action Set
Packet
In
Packet
Out
Open vSwitch
. . .
Action Set
Action Set
Action Set
Action Set
Match Fields:
Ingress port +
Packet header +
metadata
Packet transmission through flow tables within an Open vSwitch

## Slide 15: Intent

## Slide 16
Demo
Use Case-1: Testing the ONOS Controller with Isolated Layer 2 Overlay Networks

## Slide 17
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
eth4
eth14
eth1
eth1
eth1
eth3
eth2
eth2
eth2
eth2
OVS-2
OVS-6
OVS-8
OVS-4
eth1
eth4
eth1
eth5
eth14
eth14
eth14
eth14
eth14
eth3
eth5
eth4
eth3
eth5
eth3
eth3
eth2
eth1
eth3
eth2
eth4
eth5
eth1
eth3
eth2
eth1
eth3
eth2
10.0.0.2/24
10.0.0.3/24
10.0.0.10/24
10.0.0.11/24
10.0.0.12/24
H1
H2
H3
Server1
Server2
Server3
Intent

## Slide 18
ONOS-1
ONOS-3
ONOS-2
Atomix-1
Atomix-3
Atomix-2
172.17.0.2
172.17.0.3
172.17.0.4
172.17.0.5
172.17.0.6
172.17.0.7
Raft protocol
Use Case-2: Testing the Network with Multiple ONOS Controllers
Demo
Underlying network

## Slide 19
Use Case-3: Testing the ONOS Controller with IPv6 Addressing
Demo

## Slide 20
Intent

## Slide 21
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
OVS-2
OVS-8
OVS-4
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
50.0.0.1/24
60.0.0.1/24
.2
.1
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
AS 100
AS 200
AS 300
AS 400
Border R4
Border R2
Border R3
Border R1
Internal R5
Internal R6
Controller
BGP Speaker
Use Case-4: Integrating Software-defined Network with the Legacy Networks
Demo

## Slide 22
Single-point to single-point intents
These are uni-directional intents used to establish the BGP peering session between the external routers and the SDN BGP speakers. Each Intent connects two single attachment points in the SDN network. Each attachment point contains the following information: SDN switch DPID and switch port, and the MAC address of the attached BGP speaker/router.
Multi-point to single-point intents
These are uni-directional intents used to connect the hosts of the external networks together. Each intent is associated with an IP prefix (the IP destination), and connects the ingress attachment points of the SDN network with a single egress attachment point - the best next-hop router toward the destination IP prefix. At the ingress edge of the SDN network, an IP packet is matched on the IP destination address. The forwarding entry for the best (longest network prefix) match is selected to forward the packet toward the corresponding egress attachment point. In addition, right before the packet is forwarded, the “change destination MAC address” action is applied such that the data packet will contain the MAC address of the egress IP router toward the destination.

## Slide 26: SDN network components
Open vSwitch
OpenFlow

## Slide 27: SDN Architecture
Application Layer
Control Layer
Infrastructure Layer
Software-defined Network (centralised control)
Traditional Network (distributed control)
Embedded controlling and forwarding device
Northbound Interface
Southbound Interface

## Slide 28
Use Case-4: Integrating Software-defined Network with the Legacy Networks

## Slide 29
Use Case-2: Testing the Network with Multiple ONOS Controllers

## Slide 30
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
eth14
OVS-2
OVS-8
OVS-4
eth14
eth14
eth14
eth14
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
PC1
50.0.0.1/24
60.0.0.1/24
.2
.1
PC2

## Slide 31
10.0.0.1/24
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
PC1
50.0.0.1/24
60.0.0.1/24
.2
.1
PC2

## Slide 32
Switchport
VLAN ID
Src MAC
Dest MAC
OF: Match-fields
OF: Action
Src IP
Dest IP
1
Egress port 2,3
FF:FF:FF:FF:FF:FF
Ingress port
Dest MAC
VLAN ID
10
*
*
*

## Slide 35
VPLS1
VPLS1
VPLS2
VPLS2
OVS-1
OVS-2
OVS-3
OVS-4
OVS-5
OVS-6
OVS-7
OVS-8
H1
H2
S1
S2

## Slide 36
VPLS1
VPLS1
VPLS2
VPLS2
OVS-1
OVS-2
OVS-3
OVS-4
OVS-5
OVS-6
OVS-7
OVS-8
H1
H2
S1
S2
VPLS2
VPLS1
H3
S3

## Slide 37
Atomix Cluster
{
Set the cluster ID : { onos }
Set the node ID : { atomix-number }
Set the IP address of atomix container : { x.x.y.y }
Set the port number to lister to onos : { 5679 }
# List of atomix containers part of the cluster
Discovery:
{ node ID and IP address of atomix container }
# Specify the management group information for configuration of managing primitives
type : { raft }
partitions : { number of partitions }
members : { node IDs of atomix container }
# Specify the partition group information for configuration of primitive storage and replication
type : { raft }
partitions : { number of partitions }
members : { node IDs of atomix container }
  }

## Slide 38
ONOS Cluster
{
Set the name : { onos }
Set the node ID : { onos-number }
Set the IP address of onos container : { x.x.y.y }
Set the port number : { 9876 }
# Specify the information about atomix cluster
Storage:
{
IP address of atomix container : { raft }
node ID of atomix container : { raft }
port number of atomix container : { 5679 }
}
  }

## Slide 39
VPLS configuration
{
# Specify the list of Open vSwitch ports where hosts are connected
Device ID : { MAC address of logical management interface (Bridge br0) of Open vSwitch }
Interfaces : { name, MAC address and VLAN ID of the host device }
  Set the application ID of VPLS : { org.onosproject.vpls }
  # Create the list of VPLS overlay network
  Set VPLS ID : { name for VPLS }
  Add the interfaces to the created VPLS ID : { name of the host device participating in the same VPLS ID }
  Set encapsulation method for VLAN: { VLAN, MPLS or none }
  }

## Slide 40
Flows
{
  Declare priority value of flow : { 0 and 65535 }
  Set the flow entry state : { permanent=true, timeout-0 }
  Set Device ID : { MAC address of logical management interface (Bridge br0) of Open vSwitch }
  # Action to be taken by open vSwitch after the match-fields are matched
  Treatment:
  instructions: { send out the packet from port number,
  send packet to flow table number, etc. }
  # Specifying the match-fields for flow
  Selector:
  criteria: { source and destination MAC address,
  source and destination IP address,
  ingress port, VLAN ID, etc. }
  }

## Slide 41
Intents
{
  Declare the type of intent : { Host-to-Host, SinglePoint-to-MultiPoint, MultiPoint-to-SinglePoint }
  Set the application ID : { org.onosproject.ovsdb }
  Declare priority value of intent : { 0 and 65535 }
  # Specify the information of devices
  For Host-to-Host intent: { MAC address of the first and second host }
  For SinglePoint-to-MultiPoint intent: { Device ID with ingress port number & Device IDs with egress port numbers }
  For MultiPoint-to-SinglePoint intent: { Device IDs with ingress port numbers & Device ID with egress port number }
  }

## Slide 42
GNS3 Client
GNS3 Server
(GNS3 VM)
ONOS
ONOS Docker
Ryu
OpenDaylight
VirtualBox
Host machine
NIC
Mininet
Bridge
Adapter
VirtualBox
Adapter

## Slide 43
Version 1.0 | Version 1.1 | Version 1.2 | Version 1.3 | Version 1.4 | Version 1.5
Single flow table entry | Multiple flow table | Support for IPv6 | Support for IPv6 extension header | Add in bundle mechanism | Egress table
Single Controller | Pipeline Processing | Extensible TLV support | Flow meter | Support for Table synchronization | Packet type aware Pipeline
Support for IPv4 | Support for VLAN and MPLS |  | Support for Table miss |  | Extensible flow entry statistics
 | Group table |  |  |  | 
 | Virtual ports |  |  |  | 

## Slide 44
SDN Control Architecture

## Slide 45
OF:

## Slide 46
OF:

## Slide 47
2
3
4
5
6
7
9
10
13
14
16
17

## Slide 48
OF: ICMPv6 request Dest: 2001::1004
OF: ICMPv6 request Dest: 2001::1004
ICMPv6 request Dest: 2001::1004
OF: Neighbor Solicitation
TA: 2001::1004
OF: Neighbor Advertisement
TA: 2001::1004
OF: Neighbor Advertisement TA: 2001::1004
OF: ICMPv6 request Dest: 2001::1004
OF: ICMPv6 request Dest: 2001::1004
H1
Open vSwitch-1
Open vSwitch-4
2001::1001
H4
ONOS Controller
2001::1004
ICMPv6 request Dest: 2001::1004
Open vSwitch-2
Open vSwitch-3
OF:
Neighbor Solicitation
TA: 2001::1004
OF: Neighbor Solicitation TA: 2001::1004
OF: Neighbor Solicitation TA: 2001::1004
192.168.122.159
192.168.122.164
192.168.122.175
192.168.122.135
192.168.0.114
1
2
3
4
5
6
7
8
9
10

## Slide 49
OF: ICMPv6 reply Dest: 2001::1001
OF: ICMPv6 reply Dest: 2001::1001
ICMPv6 request Dest: 2001::1004
ICMPv6 reply Dest: 2001::1001
ICMPv6 reply Dest: 2001::1001
OF: ICMPv6 reply Dest: 2001::1001
OF: ICMPv6 reply Dest: 2001::1001
H1
Open vSwitch-1
Open vSwitch-4
2001::1001
H4
ONOS Controller
2001::1004
ICMPv6 reply Dest: 2001::1001
Open vSwitch-2
Open vSwitch-3
192.168.122.159
192.168.122.164
192.168.122.175
192.168.122.135
192.168.0.114
14
11
12
13
15
16
17
18
ICMPv6 request Dest: 2001::1004
ICMPv6 request Dest: 2001::1004
ICMPv6 reply Dest: 2001::1001
ICMPv6 reply Dest: 2001::1001
ICMPv6 request Dest: 2001::1004
ICMPv6 reply Dest: 2001::1001
19
20
21
22
23
24

## Slide 50
ICMPv6 request Dest: 2001::1004
ICMPv6 request Dest: 2001::1004
ICMPv6 reply Dest: 2001::1001
ICMPv6 reply Dest: 2001::1001
H1
Open vSwitch-1
Open vSwitch-4
2001::1001
H4
2001::1004
ICMPv6 request Dest: 2001::1004
ICMPv6 reply Dest: 2001::1001
2
3
4
6
7
1

## Slide 51
VPLS Manager
VPLS Config Manager
VPLS
ONOS CLI
REST API
VPLS Neighbour Handler
VPLS Operation Manager
Distributed VPLS Store
VPLS Store
VPLS Operation Service
VPLS Store delegate
VPLS Operation
Update VPLS state
Query VPLS information
Add
Remove
Update
VPLS
VPLS
Store
Event
VPLS Config Events

## Slide 53
add-test-flows
onos:add-test-flows
onos:add-test-flows [options] flowPerDevice numOfRuns

## Slide 55
Masthead
ONOS Cluster Node Panel
Topology Toolbar
Summary Panel
Navigation Menu Button
Username/
Logout link

## Slide 56
Application & Service Layer
Application Plane
Control Layer
Controller Plane
Infrastructure Layer
Data Plane
Network
Elements
SDN
Controller
SDN
Applications
Northbound Interface (NBI)
Southbound Interface (SBI)
REST API
OpenFlow, BGP, NetConf

## Slide 57
Application Layer
Control Layer
Infrastructure Layer
Software-defined Network (centralised control)
Traditional Network (distributed control)
Embedded controlling and forwarding device
Northbound Interface
Southbound Interface

## Slide 59
OVS-2
OVS-3
OVS-4
OVS-1
192.168.122.161
192.168.122.164
192.168.122.163
192.168.122.162
10.0.0.1/24
10.0.0.2/24
10.0.0.3/24
eth0
eth0
192.168.0.114
ONOS Controller
eth0
eth0
eth1
eth1
eth1
eth1
eth2
eth2
eth2
eth2
eth3
g0/0
g0/0
g0/0
R1
R2
R3
NAT
Switch

## Slide 60
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
eth4
eth14
eth1
eth1
eth1
eth3
eth2
eth2
eth2
eth2
OVS-2
OVS-6
OVS-8
OVS-4
eth1
eth4
eth1
eth5
eth14
eth14
eth14
eth14
eth14
eth3
eth5
eth4
eth3
eth5
eth3
eth3
eth2
eth1
eth3
eth2
eth4
eth5
eth1
eth3
eth2
eth1
eth3
eth2
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
PC1
50.0.0.1/24
60.0.0.1/24
.2
.1
PC2

## Slide 61
Network – technical icons (1)
IP/MPLS Routers
Router
Broadband Router
Service Router
Secure Router
Router with TDM
Content Router
IPoDWDM Router
Storage Router
Wavelength Router
Ethernet/IP Switches
Switch
Secure Switch
IP DSL Switch
TDM Switch
Content Switch
IP/MPLS Complementary - Security
Load Balancer
Load Balancer
Load Balancer Star
DSLAM
Firewall
ATM
Router with ATM
ATM Switch
Switch Router
DSLAM (ATM)
Converged Service Delivery Platform
Content Engine
Content Server
Video Server
Music Server
Application Control Engine
IP/TV Content Manager

## Slide 62
Network – technical icons (2)
Voice Platform
Media Gateway
Soft Switch
Encoder
Decoder
Transcoder
Access Gateway
Wireless Technology
Wireless Transport
Wireless Router
Base Station
NodeB
WiAN
Wireless Technology - Mobile Service Delivery Platform
Wireless Access Point
Wireless Bridge
WLAN Controller
Cell Phone
SGSN
Wireline Technology - Signaling
Digital Cross-Connect
Fixed Access Point
MSAN
SBC
Miscellaneous
Database/Storage
Gateway
Controller
Control Device
Access Device
Telephone POTS
BSC
RNC
4G Control
GGSN
MSC
STP
Miscellaneous
Telephone IP
Protocol Translator
Resource Manager
Net Sonar
Call Manager
Asic Processor
Netcrypt
Guard
FC Storage