## Slide 1: SDN based Network Management in Emulated Environment
Submitted by: Harshal Rajan Vaze
Matriculation no.: 1269879
First examiner: Prof. Dr. Ulrich Trick
Second examiner: Prof. Dr. Armin Lehmann
External supervisor: Dr. Peter Gröschke

## Slide 2: Agenda
SDN Architecture
Different SDN Architectures
Open-source SDN Controllers
Open vSwitch
OpenFlow
Creation of Flow rules
Creations of Intents
Use-cases

## Slide 3: SDN Architecture
Application & Service Layer
Application Plane
Control Layer
Controller Plane
Infrastructure Layer
Data Plane
Network
Elements
SDN
Controller
SDN
Applications
Northbound Interface
Southbound Interface
REST API
OpenFlow, BGP, NetConf
Eastbound Interface
Westbound Interface

## Slide 4: Different SDN Architectures (1/3)
a. Physically-centralised architecture
b. Physically-distributed architecture

## Slide 5: Different SDN Architectures (2/3)
c. Physically-distributed & Logically-centralised architecture
d. Physically-distributed & Logically-distributed architecture
Act like a single controller for network

## Slide 6: Different SDN Architectures (3/3)
Root controller
e. Flat architecture
f. Hierarchical architecture

## Slide 7: SDN Network Components
Different components by different communities
SDN Controllers
  ONOS
  OpenDaylight
  Ryu
Open vSwitch
OpenFlow protocol
Emulated environments

## Slide 8
Applications
North-bound (Consumer) API
Core
(Modules, Subsystems)
South-bound (Provider) API
Providers
(Link, Flow, Device, Host)
Protocols
Network Elements
ONOS Controller

## Slide 9
Applications, Orchestration
North-bound API
South-bound API
Network Elements
OpenDaylight
Platform Services
AAA
Data Exchange
Infrastructure utilities
Built-in Applications
Layer 2 Switch
Virtual Tenant Network
Network Services
LISP service
Group-based policy
Application layer traffic optimization
Platform (MD-SAL, YANG tools)
OpenDaylight Controller

## Slide 10
Applications, Operator, OpenStack cloud orchestration
North-bound API
South-bound API
Network Elements
Ryu Framework
Built-in Applications: tenant isolation, layer2 switch
Libraries: topology discovery, OpenFlow REST
OpenFlow protocols parser/ serializer
OpenFlow, OF-config
Non-OpenFlow protocols parser/ serializer
NetConf, NetFlow, VRRP
Ryu Controller

## Slide 11
Flow Tables
ovs-vswitchd
ovsdb-server
Controller
OpenFlow
Protocol
User Space
Open vSwitch
Kernel module
OVSDB Management
Protocol
OVSDB Management
Protocol
Netlink
In-Port
Out-Port
Kernel
Management
ovs-dpctl
ovsdb-tool and ovs-vsctl
ovs-ofctl and ovs-appctl

## Slide 12
Flow Table 0
Group Table
Meter Table
OpenFlow
Channel
OpenFlow
Channel
Flow Table n
Flow Table 1
Port
Port
. . .
Controller 1
Controller 2
OpenFlow
OpenFlow Switch
Pipeline
Datapath
Control Channel
OpenFlow Protocol
SBI protocol
6 major releases
Main components
  Flow table
  Group table
  Meter table
  Control channel
Three Message types:
  Controller-to-switch
  Asynchronous
  Symmetric

## Slide 13: SDN network emulators
GNS3
Client part: The GNS3-all-in-one software (GUI)
Server part: The GNS3 virtual machine (GNS3 VM)
Advantages of GNS3:
Implements easy to access network topology.
Pre-configured and optimised appliances available to simplify deployment.
Availability of in-built software packages such as Wireshark and Putty.
Supports sharing of implemented network including the device configuration.
Disadvantages of GNS3:
Limitation of CPU and memory resources provided by the host machine.
The software images of the network devices are required to be purchased and downloaded by the user.
Mininet
Advantages of Mininet:
It is very fast and takes very little time for booting.
It is easy to install and use.
It saves money because the emulators are cost-effective instead of testing with hardware devices.
It is also very easy to connect with other network devices.
Disadvantages of Mininet:
Deployed network elements cannot exceed the CPU and bandwidth available on host machine.
Single server implementation gave rise to the performance problems.
All Mininet hosts share the host file system and PID space, a careful assessment of running daemons is required for process of debugging.

## Slide 14: Flow Rules
Forwarding flow rules
Application commands >> Flow rules
Creation & Installation
  Open vSwitch CLI
  ONOS REST API
  ONOS CLI
Demo

## Slide 15
Flow
Table
0
Ingress Port
Egress Port
Flow
Table
1
Flow
Table
n
Execute Action Set
Packet
In
Packet
Out
Open vSwitch
. . .
Action Set
Action Set
Action Set
Action Set
Match Fields:
Ingress port +
Packet header +
metadata
Packet transmission through flow tables within an Open vSwitch

## Slide 16: Creation of Intents
Policy-based directives
Intent Framework is a subsystem
Application commands >> Flow rules
Creation & Installation
  ONOS CLI
  ONOS GUI
  ONOS REST API
Demo

## Slide 17
Demo
Use Case-1: Testing the ONOS Controller with Isolated Layer 2 Overlay Networks

## Slide 18
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
eth4
eth14
eth1
eth1
eth1
eth3
eth2
eth2
eth2
eth2
OVS-2
OVS-6
OVS-8
OVS-4
eth1
eth4
eth1
eth5
eth14
eth14
eth14
eth14
eth14
eth3
eth5
eth4
eth3
eth5
eth3
eth3
eth2
eth1
eth3
eth2
eth4
eth5
eth1
eth3
eth2
eth1
eth3
eth2
10.0.0.2/24
10.0.0.3/24
10.0.0.10/24
10.0.0.11/24
10.0.0.12/24
H1
H2
H3
Server1
Server2
Server3
Created Layer 2 Overlay Networks

## Slide 19
ONOS-1
ONOS-3
ONOS-2
Atomix-1
Atomix-3
Atomix-2
172.17.0.2
172.17.0.3
172.17.0.4
172.17.0.5
172.17.0.6
172.17.0.7
Raft protocol
Use Case-2: Testing the Network with Multiple ONOS Controllers
Demo
Underlying network

## Slide 20
Use Case-3: Testing the ONOS Controller with IPv6 Addressing
Demo

## Slide 21
IPv6 tunneling over IPv4 network

## Slide 22
OVS-3
OVS-5
OVS-7
OVS-1
10.0.0.1/24
OVS-2
OVS-8
OVS-4
20.0.0.1/24
10.0.0.2/24
20.0.0.2/24
30.0.0.2/24
30.0.0.1/24
40.0.0.1/24
192.168.100.0/24
50.0.0.1/24
60.0.0.1/24
.2
.1
40.0.0.2/24
50.0.0.2/24
60.0.0.2/24
AS 100
AS 200
AS 300
AS 400
Border R4
Border R2
Border R3
Border R1
Internal R5
Internal R6
Controller
BGP Speaker
Use Case-4: Integrating Software-defined Network with the Legacy Networks
Demo
SDN
AS 500

## Slide 23: Questions?

## Slide 24: Thank you!